## Slide 1: Towards Analyzing Neural Time Series Data Affected by Stimulation Artifact
Evan Dastin-van Rijn
Brown University
Senior Undergraduate

## Slide 2: Agenda
Period-based Artifact Reconstruction and Removal Method (PARRM)
Periodic Estimation of Lost Packets (PELP)
Plans for evaluating analysis approaches with missing data

## Slide 3: PARRM Motivation
Robust across sampling rates (low and high)
Flexible to varying artifact waveforms (short and long)
Robust to aliasing
Implementable in real-time
Loss agnostic

## Slide 4: Period Estimation
https://github.com/neuromotion/PARRM
Dastin-van Rijn, Evan M. and Provenza, et al. Uncovering Biomarkers During Therapeutic Neuromodulation with PARRM: Period-Based Artifact Reconstruction and Removal Method. Available at SSRN: https://ssrn.com/abstract=3748590 or http://dx.doi.org/10.2139/ssrn.3748590

## Slide 5: Period-based Artifact Reconstruction and Removal Method (PARRM)

## Slide 6: Validation of Method in Saline
Injected 10 Hz and 50 Hz signals
200 Hz sampling rate, 150 Hz stimulation frequency (alias at 50 Hz)

## Slide 7: Validation of Method in Saline
Similar in time domain
PARRM returns absolute error distribution to the level of baseline noise exceeding a template subtraction approach and notch filter

## Slide 8: PARRM Performance in-vivo

## Slide 9: PARRM Recovers Biomarker Coincident with Artifact
130 Hz stimulation obscures gamma movement biomarker during task
Biomarker is recovered following filtering using PARRM despite coinciding with stimulation artifact

## Slide 10: Motivation for PELP
PELP provides a method to exactly determine the number of samples missing due to packet losses for recordings where stimulation is on.
We validated the method using a stimulation model added to EEG data and simulated packet losses along with RC+S data in the clinic and from the patient’s own home.

## Slide 11: Packet loss
Continuous data sampled onboard are organized into discrete chunks of variable size called packets
During wireless transmission, it is possible for some packets to not be received
Lost packets result in missing data and uncertain relative timing of remaining samples

## Slide 12: Periodic Estimation of Lost Packets (PELP)
Identify locations of all packet losses
Estimate size of each packet loss using systemTick
Group contiguous packets into continuous runs
Find stimulation period using period estimation component of PARRM
Fit harmonic regression model to longest run
For each loss, compute RMSE between samples and model prediction. The loss size that minimizes RMSE is the true size
Evan M. Dastin-van Rijn, et al.
Accounting for missing data in neural time series using PELP: Periodic Estimation of Lost Packets (in preparation)

## Slide 13: Harmonic Regression Model
Sum of sinusoids with period , number of sinusoids , and coefficients
Ratio of stimulation artifact amplitude to signal amplitude R
Standard deviation of pulse amplitude V
Period drift d

## Slide 14: Simulation Features
Stimulation model is well fit to EEG data (1000 Hz sampling rate, 150.6 Hz stimulation frequency)
20% of data were randomly removed as 50 sample packets. Random removal was repeated 100 times.

## Slide 15: Validation Using Simulation
Ran a sweep of stimulation parameters as a function of uncertainty in the loss estimate (the range of difference from the estimate that were compared)
Discrete transitions occur at multiples of 3 since the period is 6.64000 samples and stimulation is bilateral
PELP is effective over a range of parameters but is most sensitive to amplitude variability

## Slide 16: Validation Using RC+S Data
PELP was applied to data from the clinic sampled at 1000 Hz and data recorded in the patient’s home at 250 Hz during the same behavioral task
15 sets of missing samples in the clinic, 121 at home
Amplitude ratio of 27 in clinic and 1.1 at home
LFP samples are well consolidated about stimulation model indicating accurate estimation of losses

## Slide 17: Packet Loss and Data Analysis
Standard approaches to filtering data, computing power spectral densities, and time frequency decomposition cannot be used for continuous recordings containing missing data
For stable recordings, packet losses can be ignored by looking at continuous runs individually and removing transient artifacts at boundaries
At home, packet losses are far more frequent and removing transients would lead to the rejection of most of the data

## Slide 18: Analyzing Data with Losses
Two general approaches:
  Loss interpolation
    Mean fill
    Linear/spline
    AR models
  Loss agnostic methods
    Normalized convolution
    Lomb-Scargle
    Adaptive wavelet transforms
Method performance depends on presence of stimulation and accuracy of loss estimates

## Slide 19: Evaluating Solutions
Use published EEG datasets with known signals of interest (ERPs, PSDs, ERSPs)
Simulate stimulation and packet losses (accurate and jittered)
Apply corrective method
Compare ability to resolve signal of interest to ground truth
Realistic noise conditions and true biological signals

## Slide 20: Acknowledgements
Baylor
  Psychiatry: Eric Storch PhD, Nithya Ramakrishan PhD, Greg Vogt, BS, Michelle Avendano-Ortega, BS, Andrew Weise, PhD
  Neurosurgery: Sameer Sheth MD, PhD, Ashwin Viswanathan MD, Mike Beauchamp PhD, Meghan Robinson PhD
  Neurology: Jay Gavvala, MD, Adriana Strutt PhD
  Radiology: Gordon Xu, PhD
  Medical Ethics: Gabe Lazaro JD, PhD, Amy McGuire JD, PhD;
Medtronic
  Rob Raike PhD, Rene Molina PhD, Thaddeus Brink, PhD
  Devices: PC/RC+S
NIH
  Nick Langhals PhD, Kari Ashmont PhD, David McMullen MD, Mi Hillefors MD, PhD, Brooks Gross, PhD
  NIH BRAIN Funding
  UH3NS100549-01 Adaptive DBS in Non-Motor Neuropsychiatric Disorders: Regulating Limbic Circuit Imbalance
Brown Engineering
  Dave Borton, PhD
  Nicole Provenza, MS
  Michael Frank, PhD
  Matthew Harrison, PhD
  Evan Dastin-van Rijn
University of Pittsburgh Psychology
  Jeff Cohn, PhD
  Yaohan Ding, PhD
Carnegie Mellon University
  Laszlo Jeni, PhD
  Itir Ertugrul, PhD
Notes: Large and scientifically diverse team: psychiatry, psychology, neurosurgery, neurology, engineering, machine learning, medical ethics, neuroanatomy and imaging.

## Slide 21: Validation of Method with Simulation