## Slide 1: Effects of Data Losses on Neural Time Series Analysis
Evan Dastin-van Rijn

## Slide 2: OpenMind Approach to Loss Estimation
PacketGenTime (default)
Unavoidable time error distribution with a standard deviation of 30 ms
No accrued error over long timescales
System Tick
Millisecond accuracy on short timescales
Large accrued error over long timescales (~20 minutes)
How does the PacketGenTime timing error impact the recovery of averaged signals?

## Slide 3: Simulation Set-up
Modeled ERPs as positive going Gaussian peaks of variable duration
Modeled neurological noise as a sum of sinusoids with random phase and 1/f distribution for amplitude
Concatenated 300 simulated trials of combined noise and ERP
Randomly added 30, 100 ms packet losses and estimated them for a range of timing errors (0-50 ms standard deviation)

## Slide 4: Measures of Interest
Additionally, simulated variable trial conditions by reducing amplitude by a factor of 0.75 for comparisons based on a t-test and Cohen’s d effect size

## Slide 5: Simulation Results
1000 simulated experiments for each combination of offset and timing error
Metrics were averaged and displayed in each heatmap

## Slide 6: Analyzing Time Series with Missing Data
Problem – cannot use standard filters, wavelet transforms, or FFTs when there are missing samples in a timeseries
Solutions
Analyze continuous segments, however, this is only possible if losses are infrequent
Use loss agnostic methods, however, they are slow and non-standard
Impute missing data, however, this may introduce artifacts at the loss and in the window affected by the loss

## Slide 7: Loss Imputation
Simulation set-up
Randomly insert 50 sample losses to remove a set percentage of the data
Apply one of four straightforward imputation methods
Estimate effect on a ground truth signal for DBS off, DBS on, and PARRM-filtered DBS on

## Slide 8: Simulation Dataset
ERP and ERSP data from an online EEG recording during a cognitive control task were used
28 healthy participants
Time domain data was low-pass filtered at 20 Hz prior to ERP computation
ERSP was computed via a continuous wavelet transform
Correct and error trials were significantly different at the group level

## Slide 9: Time Domain Correlations
Raw R2 correlation in time domain for different sample types
Losses-removed samples that were imputed
Filtered-samples in the same low-pass filter window as a loss
ERP-samples within the window of interest for the ERP

## Slide 10: Time Domain Hypothesis Testing
Top-row – plot of ERP p-value for each simulated loss experiment for 5% data loss against the original p-value for the participant. ⍺=0.05 shown by dotted line. Lines are fit for each imputation approach
Middle-row – proportion of simulated experiments that were non-significant but the original data were significant for each loss percentage
Bottom-row – slope of fit line for each loss percentage

## Slide 11: Frequency Domain Correlations
Raw R2 correlation in time domain for different sample types
Losses-removed samples that were imputed
Filtered-samples in the same wavelet convolution window as a loss
Results are shown across frequencies and for two loss percentages
ERSP-samples within the window of interest for the ERSP

## Slide 12: Frequency Domain Hypothesis Testing
Top-row – plot of ERP p-value for each simulated loss experiment for 5% data loss against the original p-value for the participant. ⍺=0.05 shown by dotted line. Lines are fit for each imputation approach
Middle-row – proportion of simulated experiments that were non-significant but the original data were significant for each loss percentage
Bottom-row – slope of fit line for each loss percentage

## Slide 13: Cognitive Control Results with RC+S
Linear interpolation used to impute losses and applied to DBS off data (top) and PARRM-filtered DBS on data (bottom)
Significant differences in the difference spectrogram are highlighted

## Slide 14: Acknowledgements
Baylor
  Psychiatry: Eric Storch PhD, Nithya Ramakrishan PhD, Greg Vogt, BS, Michelle Avendano-Ortega, BS, Andrew Weise, PhD
  Neurosurgery: Sameer Sheth MD, PhD, Ashwin Viswanathan MD, Mike Beauchamp PhD, Meghan Robinson PhD
  Neurology: Jay Gavvala, MD, Adriana Strutt PhD
  Radiology: Gordon Xu, PhD
  Medical Ethics: Gabe Lazaro JD, PhD, Amy McGuire JD, PhD;
Medtronic
  Rob Raike PhD, Rene Molina PhD, Thaddeus Brink, PhD
  Devices: PC/RC+S
NIH
  Nick Langhals PhD, Kari Ashmont PhD, David McMullen MD, Mi Hillefors MD, PhD, Brooks Gross, PhD
  NIH BRAIN Funding
  UH3NS100549-01 Adaptive DBS in Non-Motor Neuropsychiatric Disorders: Regulating Limbic Circuit Imbalance
Brown Engineering
  Dave Borton, PhD
  Nicole Provenza, MS
  Michael Frank, PhD
  Matthew Harrison, PhD
University of Pittsburgh Psychology
  Jeff Cohn, PhD
  Yaohan Ding, PhD
Carnegie Mellon University
  Laszlo Jeni, PhD
  Itir Ertugrul, PhD
Notes: Large and scientifically diverse team: psychiatry, psychology, neurosurgery, neurology, engineering, machine learning, medical ethics, neuroanatomy and imaging.